## Slide 1
Case study – Intermediary presentation
Gasoline vs electric car
Life Cycle Assessment(LCA)

## Slide 2: Needs and objectives
Objective: Compare the environmental impacts of a gasoline vs an electric car
Study various electricity sources and different distances driven over the car lifetime
Context and needs: - Climate change and carbon emissions = large problem
- In 2019 the transportation sector generated 29% of GHG emissions in USA, largest share of emissions (US EPA 2021)
- Over 90 percent of the fuel used for transportation is petroleum based, which includes primarily gasoline and diesel (IPCC 2007)
- Lithium Ion battery production requires mining and extraction of specific metals and minerals, which also has substantial environmental impacts

## Slide 3: Function
PRODUCTS
MAIN FUNCTION
SECONDARY FUNCTION & OTHER PERFORMANCES
Product A
Product B
Transportation of people and goods
Impress others, safety,

## Slide 4: Reference flows and key environmental parameters
PRODUCTS OR SYSTEM
REFERENCE FLOWS (what is purchased)
KEY ENVIRONMENTAL PARAMETERS (linking reference flows to functional unit)
FUNCTIONAL UNIT (service offered)
Gasoline car
Electric car
1 Vehicle km
(V-km)
1/150,000 of a gas car
6.19 kg gas
Fuel efficiency
Total distance driven over lifetime
Car weight and material composition
1/225,000 of an electric car
0.26 kWh electricity

## Slide 5: Main assumptions and data used
Lifetime distance: - Gasoline car: 150000 km
Electric car: 1.5 x distance of the gasoline car
Gasoline car: input data from ecoinvent documentation: petrol car 2010 x 1.05 for weights, and / 1.05 for consumption and emissions, consumption of 0.065/1.05 kg gasoline/V-km
- Electric car : input data from conference paper Tesla 3.0
- No battery replacement

## Slide 6: Process Tree: Gasoline car – summary Neil
1 vehicle km
during 150,000 km lifespan
Transportation
Truck
3.94E-04 t-km
1 Gas Vehicle
Transportation
Freight Train
3.71E-03 t-km
Transportation
Oceanic freight
6.93E-02 t-km
alkyd paint, white
2.91E-05 kg
Note: For direct comparisons, we assume the same weight and distances divided by a different lifespan. The exact numbers calculated will be different for transportation.
aluminum, primary, ingot
3.63E-04 kg
sheet rolling, copper
1.41E-04 kg
electronics, for control units 4.08E-05 kg
ethylene
1.30E-04 kg
ethylene glycol
3.36E-05 kg
flat glass, uncoated
2.11E-04 kg
heat, natural gas
1.55E-02 MJ
lead
9.10E-05 kg
chromium oxide, flakes
1.68E-05 kg
Light fuel oil, burned in furnace 1MW of greenhouse/MJ
4.41E-04 MJ
nickel
9.80E-06 kg
polyethylene, high density, granulate
7.14E-04 kg
polypropylene, granulate
3.43E-04 kg
polyvinylchloride, suspension polymerized
1.12E-04 kg
section bar rolling, steel
1.42E-03 kg
sheet rolling, steel
3.79E-03 kg
steel, low-alloyed, hot rolled 6.93E-03 kg
sulfuric acid
5.60E-06 kg
synthetic rubber
3.09E-04 kg
tap water
2.25E-02 kg
zinc
4.12E-05 kg
electricity, medium voltage
4.16E-03 kWh
Direct combustion 6.19E-02 kg
Supply chain petrol, low-sulfur 6.19E-02 kg
zinc in car shredder residue incineration
4.12E-05 kg
glass incineration 2.11E-04 kg
emulsion paint incineration
2.91E-05 kg
plastic mixture incineration 4.55E-04 kg
aluminum recycling 3.63E-04 kg
Notes: Note: For direct comparisons, we assume the same weight and distances divided by a different lifespan. The exact numbers calculated will be different for transportation.

## Slide 7: Process Tree: Electric car summary Neil
Note: For direct comparisons, we assume the same weight and distances divided by a different lifespan. The exact numbers calculated will be different for transportation.
1 vehicle km
during 225,000 km lifespan
Transportation
Truck
2.63E-04 t-km
1 Electric Vehicle
Transportation
Freight Train
2.47E-03 t-km
Transportation
Oceanic freight
4.24E-02 t-km
alkyd paint, white
1.85E-05 kg
Battery, Li-ion, rechargeable, prismatic
3.64E-04 kg
Copper
1.28E-03 kg
electronics, for control units 1.04E-04 kg
ethylene glycol
6.49E-05 kg
extruded and thermoformed plastic sheets
7.24E-04 kg
flat glass, uncoated
2.18E-04 kg
lubricating oil
1.51E-05 kg
Metal working, aluminum manufacturing
3.40E-04 kg
Polypropylene, granulate
7.24E-04 kg
Polyurethane, rigid foam
4.04E-05 kg
steel, low-alloyed, hot rolled 4.24E-03 kg
synthetic rubber
2.37E-04 kg
electricity, medium voltage
0.26 kWh
plastic, mixture at landfill
7.24E-04 kg
glass at landfill 2.18E-04 kg
Recycling of iron and mixed metal scrap 4.25E-03 kg
mineral oil incineration
1.51E-05 kg
aluminum recycling 3.40E-04 kg
Metal working, steel manufacturing
4.24E-03 kg
waste polyurethane foam
4.04E-05 kg
Notes: Note: For direct comparisons, we assume the same weight and distances divided by a different lifespan. The exact numbers calculated will be different for transportation.

## Slide 8: Energy, CO2 and CO2equ balance: Gasoline car

## Slide 9: Energy, CO2 and CO2equ balance: Electric car

## Slide 10: Comparison of energy and CO2 balance across scenarios

## Slide 11: Interpretation – sensitivity study cumulative

## Slide 12: Interpretation – sensitivity study fossil CO2 per V-km

## Slide 13: Conclusion and next steps
The gas vehicle scenario generates higher environmental impacts in terms of energy use and carbon footprint compared to the electric vehicle with UCTE electricity, medium voltage production mix.
However, the electric vehicle scenario with hard coal generates higher environmental impacts in terms of carbon footprint compared to the gas vehicle.
The performance of electric vehicles drastically improves with wind or photovoltaic electricity – a key change towards sustainable consumption
Use phase is dominant for the gasoline and the electric car with EU mix, but manufacturing has a substantial contribution with improved photovoltaic and wind electricity